## Slide 1: Machine Learning for Methane Adsorption Capacity Prediction in Metal Organic Frameworks
Presented by GUPTA AVANI (G2303786B)

## Slide 2: Methane
Excellent candidate for alternative transport fuel
Abundant
Clean burning process
Largest combustion energy released per unit carbon dioxide emitted
Need for development of
methane capture systems!
BUT…
Responsible for 30% of the rise in global temperature
GWP of 83 times that of carbon dioxide

## Slide 3: The Solution The Problem
Zeolites
Aluminosilicate minerals containing alkali and alkaline earth metals
CH4 uptake of only ~ 100 cm3
Metal Organic Frameworks
3D networks of organic ligands with metal sites
Versatile and tunable structures
CH4 uptake >> 100 cm3

## Slide 4: The Solution The Problem
GCMC Simulations
Large number of potential MOF structures
Computationally expensive and time-taking
Need for complex and specialized software (RASPA, poreblazer, Zeo++)
Machine Learning
High accuracy
Quick response
Low computational cost
User-friendly

## Slide 5: Dataset Features
Pore Limiting Diameter
In Angstroms
Diameter of smallest opening - determines what size of molecules can enter
Gravimetric Surface Area
In m2/g
Surface area per unit mass
Largest Cavity Diameter
In Angstroms
Diameter of largest cavity - determines no. and/or size of molecules that will fit in a pore
Volumetric Surface Area
In m2/cm3
Surface area per unit volume

## Slide 6: Dataset Features
Density
In g/cm3
Mass per unit volume
Pore Volume
In cm3/g
Total volume of pores per unit mass of material
Void Fraction
Porosity
Ratio of volume of pores to volume of material
Probes 1, 2, 3 & 4
Energy-based descriptors
Average value of Boltzmann factor at all positions

## Slide 7: 1 bar 5.8 bars 65 bars Target Variable
Methane Adsorption Capacity
Adsorption capacity of metal organic frameworks for methane at constant temperature of 298 K and different pressures.

## Slide 8: Feature Correlation
Key findings:
At low pressures - Energy-based descriptors are most strongly correlated with target.
At high pressures - Void fraction and VSA are most strongly correlated with target.

## Slide 9: ML Algorithms Used
Decision Tree Regressor
Non-linear, easy to interpret
Lasso Regressor
Performs feature selection, reduces model complexity
Random Forest Regressor
High accuracy, reduces overfitting, robust to outliers and noise
Support Vector Regressor
Non-linear model, robust to outliers

## Slide 10: Model Performance
65 bars
5.8 bars
1 bar
Random Forest Model performed better than others at all pressures.

## Slide 11: Model Performance
1 bar
R2 - 0.944
MSE - 0.057
5.8 bars
R2 - 0.939
MSE - 0.062
65 bars
R2 - 0.960
MSE - 0.042

## Slide 12: Feature Importance Analysis 1 bar 5.8 bars 65 bars
Probe 3
Probe 2
Probe 4
Probe 3
Probe 2
Void Fraction
Void Fraction
GSA
VSA
Energy-based descriptors dominate at lower pressures, whereas structural descriptors are more important at higher pressures.
Insights on pressure-dependent gas adsorption mechanism.
Similar to feature correlation with target.

## Slide 13: Applications & Significance
Applications of ML Model
Material selection for MCS design
Better understanding of the adsorption process
Tune to predict adsorption of other gases
Industrial & Environmental Significance
Guide and aid experimental research
Lesser concentration of methane in atmosphere
Increased use of methane as transport fuel

## Slide 14: Conclusion
ML for Capacity Prediction
Quick, user-friendly and low computational cost.
Random Forest & its Accuracy
Best performance at all pressures with accuracy > 93%.
Significance
Leads to a more environmentally conscious world.
Future Work
Explore chemical descriptors and unsupervised and reinforcement algorithms.

## Slide 15: References
  Fanourgakis, G. S., Gkagkas, K., Tylianakis, E., Klontzas, E., & Froudakis, G. (2019). A robust machine learning algorithm for the prediction of methane adsorption in nanoporous materials. The Journal of Physical Chemistry A, 123(34), 6080-6087. https://doi.org/10.1021/acs.jpca.9b04339.​
  Feng, W., Sui, H., Tu, J., Huang, W., & Sun, K. (2018). A novel change detection approach based on visual saliency and random forest from multi-temporal high-resolution remote-sensing images. International Journal of Remote Sensing, 39(22), 1-24. https://doi.org/10.1080/01431161.2018.1479794.​
  He, Y.; Zhou, W.; Qian, G.; Chen, B. Methane Storage in Metal–Organic Frameworks. Chem. Soc. Rev. 2014, 43 (16), 5657–5678. https://doi.org/10.1039/C4CS00032C.​
  Wu, H.; Simmons, J. M.; Liu, Y.; Brown, C. M.; Wang, X.-S.; Ma, S.; Peterson, V. K.; Southon, P. D.; Kepert, C. J.; Zhou, H.-C.; Yildirim, T.; Zhou, W. Metal–Organic Frameworks with Exceptionally High Methane Uptake: Where and How is Methane Stored? Chem. – Eur. J. 2010, 16 (17), 5205–5214. https://doi.org/10.1002/chem.200902719.​
  Machine Learning Using Combined Structural and Chemical Descriptors for Prediction of Methane Adsorption Performance of Metal Organic Frameworks (MOFs) | ACS Combinatorial Science. https://pubs.acs.org/doi/10.1021/acscombsci.7b00056 ​
  Global Warming Potential. Wikipedia; 2024.​
  Review and Analysis of Molecular Simulations of Methane, Hydrogen, and Acetylene Storage in Metal–Organic Frameworks | Chemical Reviews. https://pubs.acs.org/doi/full/10.1021/cr200217c ​

## Slide 16: Thank you!